## Slide 1
Zephyr RTOS Power Management (PM) Optimizing energy efficiency in embedded system

## Slide 2
Zephyr RTOS Power Management (PM)
The Power Management subsystem in Zephyr enables developers to optimize energy consumption in embedded systems by leveraging SoC hardware features.
Core Components
System Power Management (System PM): Controls the entire system’s power state (e.g., sleep, deep sleep, suspend).
Device Power Management (Device PM): Manages power states of individual devices (drivers, peripherals).
Device Runtime PM: Dynamically manages device power states at runtime, based on usage.
Power Domains: Logical grouping of devices that share a common power source, allowing coordinated power control.
System Power Management = global states;
Device Power Management (Device PM = per-device states.
Runtime PM
Automatic suspend/resume based on usage (reference counting).
What are Power Domains
Groups of devices sharing a power source, managed together.

## Slide 3
Layer | Responsibility
Application | Requests power-saving policies or device usage.
System PM | Decides global system state (idle, sleep, deep sleep).
Device PM | Manages device-level states (active, suspended, off).
Runtime PM | Automatically suspends/resumes devices based on activity.
Power Domains | Groups devices for coordinated power transitions.
Hardware (SoC) | Provides low-power modes, wakeup sources, clock gating.
RTOS Power Management (PM) Architecture
System PM: Decides when the whole system can sleep.
Device PM: Ensures individual devices are powered down when not needed.
Runtime PM: Automates device PM, so developers don’t need to manually suspend/resume every time.

## Slide 4
- Application sets the rules
- System PM manages the big picture
- Device PM manages peripherals
- Runtime PM automates usage-based control
- Power Domains optimize groups of devices
- Hardware enforces the actual power savings
RTOS Power Management (PM) Architecture

## Slide 5
Zephyr RTOS – System Power Management
System Power Management (System PM) is the part of Zephyr’s Power Management subsystem that controls system-wide low-power states when the kernel is idle. It ensures efficient energy usage while balancing performance and wakeup latency.
System PM manages global system states (idle, sleep, deep sleep). It is architecture- and SoC-independent, achieved by separating the core PM infrastructure from SoC-specific implementations.
- The Policy Manager is the decision‑making component of System Power Management.
- Policy Manager selects power state that decides which power state to enter.
- Residency‑based policy → automatic, based on idle time vs. latency
- Application‑defined policy → developer logic via pm_policy_next_state()
Residency‑based policy = automatic, math‑driven, based on idle time vs. latency.
- Application‑defined policy = custom, rule‑driven, developer decides via pm_policy_next_state().

## Slide 6
Residency‑Based Policy (Automatic)
- Automatic decision‑making: The framework itself chooses the deepest possible low‑power state.
- It compares:
- Expected idle time (how long the system will be inactive)
- Minimum residency (the minimum time a state must be entered to be worthwhile)
- Exit latency (time needed to wake up from that state)
- If (idle_time ≥ min_residency + exit_latency), the system can safely enter that state.
Example Scenario
- System idle time predicted: 100 ms
- Deep Sleep requires: 50 ms residency + 10 ms exit latency = 60 ms
- Since 100 ≥ 60, pm_policy_next_state() selects Deep Sleep.
Residency‑Based Policy (Automatic)

## Slide 7
Application-defined Policy (pm_policy_next_state())
Instead of letting the system decide, the application developer writes custom logic in the function pm_policy_next_state().
This function tells the PM framework which state to enter, based on application-specific rules.
Custom Logic (Application-Defined)
Developers can override pm_policy_next_state() with their own logic.
Example:
Prevent deep sleep if BLE is connected.
Force shallow sleep if a sensor read is scheduled soon.
Allow deep sleep only during certain time windows.
- pm_policy_next_state() = the decision function for choosing the next system power state.
- By default → uses residency-based automatic logic
Application-defined Policy (pm_policy_next_state())

## Slide 8
Zephyr RTOS – Device Power Management

## Slide 9
Zephyr RTOS – Device Power Management
Device Power Management (Device PM) in Zephyr provides mechanisms to control the power states of individual devices (drivers, peripherals) in a coordinated way. It ensures devices are only powered when needed, saving energy while maintaining system stability
Runtime PM is dynamic and per‑device, while System‑Managed PM is tied to system‑wide sleep states.
Device Runtime PM: Automatically suspends/resumes devices based on usage (reference counting).
System-Managed Device PM: Suspends/resumes devices when the system enters/exits low-power states.
Device States (pm_device_state): ACTIVE, SUSPENDING, SUSPENDED, OFF.
Device Actions (pm_device_action): SUSPEND, RESUME, TURN_OFF, TURN_ON.
Busy Status Indication: Mechanism to prevent suspending a device during critical operations.
Wakeup Capability: Some devices can wake the system from sleep (e.g., GPIO, RTC).

## Slide 10
APIs:
  pm_device_action_cb_t() – driver callback for suspend/resume actions.
  pm_device_busy_set()/clear() – mark device as busy or idle.
  pm_device_wakeup_enable() – enable device as wakeup source.
Macros:
  PM_DEVICE_DEFINE, PM_DEVICE_DT_DEFINE – define PM resources for drivers.
  PM_DEVICE_GET – retrieve PM context.
Config Options:
  CONFIG_PM_DEVICE – enable device PM.
  CONFIG_PM_DEVICE_SYSTEM_MANAGED – enable system-managed PM.
  CONFIG_PM_POLICY_DEVICE_CONSTRAINTS – allow devices to declare constraints.
  device states in Zephyr :
  ACTIVE, SUSPENDING, SUSPENDED, OFF.
Application requests a device (e.g., UART).
Driver resumes the device if suspended.
Framework updates reference counts and ensures dependencies are active.
When idle, Runtime PM suspends unused devices automatically.
If the System PM enters deep sleep, all devices are suspended in order.
Hardware executes the low-power transition until a wakeup event occurs.

## Slide 11
Zephyr RTOS – Device Runtime Power Management

## Slide 12
Device Power Management State Transitions in Zephyr
ACTIVE :: Device is fully powered and operational. Interrupts, bus communication, and enable pins are active.
SUSPENDED :: Device is temporarily disabled to save power. Interrupts are disabled, enable pin is low, but device can be resumed quickly.
OFF :: Device is completely powered down. Enable pin is disconnected or input to avoid back-powering. Requires reinitialization to use again.
ON :: Device is powered but not yet resumed. Typically configured into a safe/reset state before moving to ACTIVE.
Transitions
ACTIVE → SUSPENDED: Triggered by pm_device_action(SUSPEND). Saves power while keeping context.
SUSPENDED → ACTIVE: Triggered by pm_device_action(RESUME). Restores device functionality.
SUSPENDED → OFF: Triggered by pm_device_action(TURN_OFF). Fully powers down device.
OFF → ON: Triggered by pm_device_action(TURN_ON). Prepares device for use.
ON → ACTIVE: After initialization/configuration, device becomes fully operational.

## Slide 13
Zephyr RTOS – Power Domains

## Slide 14
A Power Domain in Zephyr is a logical grouping of devices that share a common power source. Instead of managing each device individually, the system can control the entire domain, turning multiple devices on/off together. This reduces leakage currents and improves energy efficiency.
A group of devices sharing a common power source, managed together for energy efficiency.
Internal domains are SoC regions grouped for power gating; external domains are powered by regulators, switches, or PMICs outside the SoC.
Instead of managing each device individually, the system can control the entire group together.
This is especially useful when multiple peripherals depend on the same supply.
Zephyr RTOS – Power Domains
Core Components
Power Domain: A group of devices powered by the same source (internal SoC region or external regulator).
Internal Power Domain: A region inside the SoC grouping devices that can be powered down together.
External Power Domain: Devices outside the SoC powered by external regulators, switches, or PMICs.
PM Device Action: Notifications sent to devices when their domain changes state (TURN_ON, TURN_OFF, SUSPEND, RESUME).
Wakeup Source: A device in a domain that can wake the system from low-power mode.

## Slide 15
Key Components
Config Option: CONFIG_PM_DEVICE_POWER_DOMAIN – enables power domain support.
Devicetree:
  compatible = "power-domain" – marks a node as a power domain.
  power-domains = <&domain> – associates a device with a domain.
APIs:
  pm_device_children_action_run() – notifies all devices in a domain.
  pm_device_action_cb_t() – driver callback for handling domain actions.
Key Components Power Domains

## Slide 16
Workflow
1) Definition in Devicetree
- A power domain is declared as a node (e.g., regulator, PMIC, or SoC block).
Devices reference it using the power-domains property.
2) Domain ON/OFF
- When the domain is ON, all devices inside it are powered and can operate.
When the domain is OFF, all devices inside it lose power and must be suspended.
3) Device Notification
- The PM framework notifies devices in the domain when the domain changes state.
Drivers implement callbacks to handle TURN_ON and TURN_OFF actions.
4) Wakeup Sources
- Some devices in a domain may act as wakeup sources (e.g., GPIO, RTC).
- Applications or drivers must configure them before the domain is powered down.
Power Domains Work Flow
Workflow Example
Step 1: Application decides Wi‑Fi + Bluetooth radios are idle.
Step 2: PM framework powers down the radio domain (shared regulator).
Step 3: Both Wi‑Fi and Bluetooth drivers are notified → they suspend.
Step 4: Later, when Wi‑Fi is needed, the domain is powered ON again → both radios resume.

## Slide 17
Comparison of System PM vs Device PM vs Power Domains
Aspect | System PM | Device PM | Power Domains
Scope | Entire system (CPU + SoC) | Individual devices (drivers, peripherals) | Group of devices sharing a power source
Control | Kernel idle thread + policy manager | Device drivers + PM framework | Domain controller (internal SoC region or external regulator)
When Applied | During idle/system-wide low-power states | When devices are unused or system suspends | When powering ON/OFF a shared rail or regulator
Granularity | Coarse (whole system) | Medium (per device) | Group-level (multiple devices together)
States Managed | Idle, Sleep, Deep Sleep, Suspend | ACTIVE, SUSPENDING, SUSPENDED, OFF | TURN_ON, TURN_OFF (domain-level)
Wakeup Sources | RTC, GPIO, timers | Device-specific (e.g., UART, sensor) | Domain-level devices (e.g., GPIO bank, radio)
Advantages | Maximizes global energy savings | Fine-grained control, runtime automation | Reduces leakage current, simplifies group control
Limitations | Risk of latency if too deep a state | Requires careful driver implementation | Dependencies and wakeup sources must be managed
Use Case Example | MCU sleeps until timer interrupt | Suspend UART when idle | Power down all sensors on shared regulator